SSCS Chipathon 2025 - Project Proposal
Time Transcenders
Hari Preeth
Shaikh Shoeb Dawood
Yuan Yancey Labay
Vasil Yordanov

---
Mixer design in GF180MCU
Targeting an active double-balanced mixer at WiFi freq 2.4GHz
Advantages of double-balanced mixers over other mixer types:
- Increased linearity
- Improved suppression of spurious products
- Good isolation between ports
- interchangeable ports, thus easy filtering
Disadvantages:
Relatively high LO drive strength
Require transformer Baluns (if time permits these will be integrated on-chip)
Decided on Gilbert cell topology (other possibilities are ring diode, star diode, or FET as switches)
https://www.qsl.net/va3iul/RF%20Mixers/RF_Mixers.pdf

---
Specs
- Target fRF 2.4GHz
- fLO 2.41GHz
- RF BW of 20MHz, with max 3dB droop over the baseband
- Vdd=3.3V
- Mixer conversion gain >15dB
- SSB NF<9dB (baseband integrated from 1kHz to 100MHz)
- IIP2 > 40dBm
- IIP3 > 8dBm ( using 2 tones at 2400MHz and 2401MHz )
https://link.springer.com/article/10.1007/s11277-021-09115-6
https://ieeexplore.ieee.org/document/7280025
Sushmitha, D & Munivenkatappa, Nagabushanam. (2018). A 2.4GHz CMOS Double Balanced Down Conversion Gilbert Cell Mixer Design Using 180nm Technology. 1767-1770. 10.1109/RTEICT42901.2018.9012334.

---
Testing equipment
Using either a 2 port Vector Network Analyzer (VNA) + signal generator
Or using a 4-port VNA
- Conversion Loss
- Intermodulation measurement
- Port isolation measurement
https://scdn.rohde-schwarz.com/ur/pws/dl_downloads/dl_application/application_notes/1ez58/1EZ58_0E_Mixer-Measurements_ZVA-K4.pdf?utm_source=chatgpt.com

---
Appendix
`

---
Conversion gain
Mixer conversion gain >15dB
- ratio of desired IF signal (V or W) to RF signal
- Voltage gain = rms(IF)/rms(RF) - we will use this def in our specs
- Power gain = IF power delivered to load / Available power from souce
Note: if load and input Z are matched, Power gain = Voltage gain

---
Noise figures: SSB
SSB Noise Figure < 9dB (baseband integrated from 1kHz to 10MHz)
- signal from one sideband, noise from both bands
- (SNR at IF) / (SNR of RF), both measured in a single sideband
https://markimicrowave.com/technical-resources/application-notes/a-practical-guide-to-noise-in-frequency-conversions/

---
Intermodulation Intercept Point (IIP)
IIP3 and IIP2 referrer to the third and second order harmonics generated from the main signal. IIP3 and IIP2 are the intercept points, at which the power of these harmonics equals the linear term (IF).
- IIP2 > 40dBm
- IIP3 > 8dBm ( using 2 tones at 2400MHz and 2401MHz )
https://www.rfwireless-world.com/terminology/ip2-ip3-formulas-calculations-significance
https://www.test-and-measurement-world.com/measurements/rf/rf-mixer-testing?utm_source=chatgpt.com

---
References
https://www.ee.iitm.ac.in/vlsi/courses/ee6320_2022/start
- https://www.ee.ucla.edu/~brweb/teaching/215C_W2013/Noise.pdf
- http://class.ece.iastate.edu/djchen/ee507/Mixer%20Design.pdf
- https://www.qsl.net/va3iul/RF%20Mixers/RF_Mixers.pdf
- https://www.test-and-measurement-world.com/measurements/rf/rf-mixer-testing?utm_source=chatgpt.com
- https://www.inf.ufrgs.br/sim-emicro/papers/emicro_palestra_inter_edgar.pdf
- https://www.rfwireless-world.com/terminology/ip2-ip3-formulas-calculations-significance
- https://markimicrowave.com/technical-resources/application-notes/a-practical-guide-to-noise-in-frequency-conversions/
- 339560320_A_24GHz_CMOS_Double_Balanced_Down_Conversion_Gilbert_Cell_Mixer_Design_Using_180nm_Technology
- https://www.youtube.com/watch?v=8qBpyJxSngo
- https://www.youtube.com/watch?v=sIyr0oMOsVc&pp=0gcJCfwAo7VqN5tD
- https://www.test-and-measurement-world.com/measurements/rf/rf-mixer-testing?utm_source=chatgpt.com